FINAL REPORT OF THE SERIOUS INCIDENT

,,TYROLEAN AIRWAYS”WITH AIRCRAFT

FOKKER  F28  Mk100 ,,OE-LVI” Nr.3/2005

In accordance with Annex 13 of the Convention of Chicago as well as the Directive 94/56/EC of 21 November 1994 establishing the fundamental principles governing the investigation of civil aviation accidents and incidents of the Council of the European Union, the purpose of an investigation conducted under the responsibility of the Latvian Accident and incident investigation division is not to apportion blame or liability.

Head of Accident and incident

Investigation division

Riga, July 2005

CONTENTS

GENERAL INFORMATION OF THE SERIOUS INCIDENT

THE INVESTIGATION

SYNOPSIS

1. FACTUAL INFORMATION

1.1 History of Flight

1.2 Injuries to Persons

1.3 Damage to Airplane

1.4 Other Damage

1.5 Personnel Information

1.6.Airplane Information

1.7 Meteorological Information

1.8 Aids to Navigation

1.9 Communications

1.10 Airport Information

1.10.1 Air Traffic Control Information

1.11 Flight Recoders

1.11.1 Cockpit Voice Recoder

1.12 Wreckage and Impact Information

1.13 Medical Information

1.14 Fire

1.15 Survival Aspects

1.16 Tests and Research

1.17 Organizational and Management Information

1.18 Additional Information

2 ANALYSIS

3 CONCLUSIONS

4 PROBABLE CAUSE

5 RECOMMENDATIONS

6 APPENDICES

GENERAL INFORMATION OF THE SERIOUS INCIDENT

Unless stated otherwise all times in this report are UTC time.

Registered Owner:			Austrian Airlines Lease and

Finance Company Ltd

Operator:				Tyrolean Arways

Aircraft type:			Fokker F28 Mk100

Nationality:				Austria

Registration:			OE-LVI

Place of Serious Incident:	Riga International Airport

Date and Time:			19 May 2005 at 13.15 hrs UTC

THE INVESTIGATION

The serious incident was notified to the Aircraft Accident and Incident Investigation Division of the Ministry of Transport of the Republic of Latvia on May 19th 2005 at 13.15 UTC and the investigation began on 19 May 2005. when additional details of the incident became known.

The Aircraft Accident and Incident Investigation team comprised Mr Ivars Gaveika (Investigator-in- Charge), Mr Ivars Zorgenfreijs (Operations )

Synopsis

The incident occurred at the route St.Petersburg-Vienna. During cruise at FL340 the crew noticed an increase in cabin altitude without any crew action to the pressurization system. The crew requested and initiated a descent after coordination and approval from ATC. During descent at the same time ”Cabin ALT” warning comes on. This was followed by an emergency descent and the Captain decided to perform landing in Riga International Airport. Oxygen masks dropped out automatically during descent at cabin altitude of 14 500 feet. After passing the altitude of 5000 feet pressurization system start’s to operate normally again. Landing was performed without any remarks.

Meteorological condition in EVRA 191250Z 32008KT 9999 13/00 Q1022 NOSIG.

1. Factual Information

1.1 History of the incident

-Flight number – OS 612, 50 passengers and 5 crew on board

-Point of departure – St.Petersburg (ULLI)

-Time of departure – 11.54UTC

-Point of destination – Vienna (LOWW)

-Point of landing – Riga (EVRA)

-Time of landing – 13.15 UTC

The slow decompression occurred during cruise FL340. At the same time ”Cabin Alt” warning comes on. Captain decided to perform emergency landing in Riga International Airport. Oxygen masks dropped out automatically during emergency descent when cabin altitude reached 14500 feet. During descent after passing the altitude 5000 feet pressurization system start’s to operate normally again. Landing was performed without any remarks.

1.1.1.Fokker F28 Mark100 REG:OE-LVI, FLN OS 612 after landing at Riga airport (EVRA) on 19.05.2005.

1.1.2. Oxygen masks dropped out automatically during emergency descent Fokker F28 Mark100, REG: OE-LVI, FLN: OS612, on 19.05.2005. (right side).

1.1.3. Oxygen masks dropped out automatically during emergency descent Fokker F28 Mark100, REG: OE-LVI, FLN: OS612, on 19.05.2005. (left side).

1.2 Injuries to persons

None.

1.3 Damage to aircraft

None

1.4 Other damage

None

.

1.5 Personnel information

The flight crew on aircraft was qualified and current to operate the flights on Fokker F70/100.

The Captain, age 52, Franz List, of ,,Tyrolean Airways” aircraft Fokker F 28 Mk0100 OE-LVI flight number OS 612 had a total of 16100 flying hours of which 8000 hours were on type, including flight hours as a Captain on Fokker F28 Mk0100.

By day of the incident had a total 04.45 flight hrs and 09.30 hrs duty time.

He held an airline transport pilot certificate and medical certificate valid until 13.11.2005. Proficiency check 13.11.2005.

The First Officer, age 50, Walter Kopejtka.of ,,Tyrolean Airways” aircraft F 28 Mk0100 OE-LVI had a total of 8500 flying hours of which 21 hours were on type. By day of the incident had a total 03.12 flight hrs and 05.05 hrs duty time.

He held an airline transport pilot certificate and medical certificate valid until 11.09.2005. Proficiency check 06.07.2003.

1.6 Aircraft information

The Aircraft Fokker F Mk0100, OE-LVI serial number 11468, manufacture by Fokker Aircraft Corporation at 1993, had a total of 39800 flying hours and 23038 landings.

Take-off weight actual – 40400 kg. (Max take off weight 44450 kg).

Balance – according operation limits and requirements.

Landing weight actual – 38 800 kg

Take-off fuel – 5900 kg

Type of fuel used – JET A-1,

1.7 Meteorological information

1.7.1 SALV31 METAR EVRA 191250z :

32008KT 9999 SCT049 13/00 Q1022 NOSIG.

1.7.2 SARS31 METAR ULLI 191045Z 191221 23008MPS 6000 BKN010CB

TEMPO 1218 1500SHRA BKN005 TEMPO 1821 0400 FG VV002

1.8 Aids to Navigation

- VOR/DME – RIX – 113,700 MHz – H24;

- LLZ RWY 36 ILS CAT 1 – IRP -  110,300 MHZ – H24;

- GP RWY 36 – 335,000 MHz – H24;

- DME RWY 36 – IRP – 1001,000 MHz,  1064,000 MHz – H24

1.9 Communications

The correct phraseology, to be used by air traffic controllers, is to be found in International Civil Aviation Organisation Doc.4444 Procedures for Air Navigation Services ,,Air Traffic management’’Chapter 7 – Aerodrome and Meteorological Information item 7.3.1.2.1 and 7.3.1.2.2.

1.10 Aerodrome information

Riga International Airport is served by one Runway18/36.

Dimensions of Rwy (M) – 2550x45

Slope of Rwy 18 – 0,05%; Rwy 36 – 0,05%;

TORA – 2550m;

TODA – 2950m;

ASDA – 2550m;

LDA –    2550m.

Surface of Rwy – Asphalt-Concrete. Note – composite construction.

PCN: 110/F/A/W/T.

Approach and Runway Lighting:

Rwy18:

-APSH LGT Type LEN INST – ALSF-1 (CAT 1) 900m spacing 30m;  LIH

-THR LGT color WBAR – Green;

-VASIS (MEHT) PAPI – PAPI left GP 3,00 degrees (62,7 feet);

-TDZ LGT LEN – NIL;

-Rwy Centre Line LGT Length spacing color, INTST –NIL;

-Rwy edge LGT LEN spacing color, INTST – 2550m , 60m white, last 600m yellow,

LIH.

-Rwy  End LGT Length spacing, color, WBAR – Red.

- SWY  LGT  LEN (m) colour – NIL

Rwy36:

APSH LGT Type LEN INST – ALSF-1 (CAT 1) 840m spacing 30m;  LIH

-THR LGT color WBAR – Green;

-VASIS (MEHT) PAPI – PAPI left GP 3,00 degrees (68,2 feet);

-TDZ LGT LEN – NIL;

-Rwy Centre Line LGT Length spacing color, INTST –NIL;

-Rwy edge LGT LEN spacing color, INTST – 2550m , 60m white, last 600m yellow,

LIH.

-Rwy  End LGT Length spacing, color, WBAR – Red.

- SWY  LGT  LEN (m) colour – NIL

1.11 Flight recorders

Flight Data Recorder (FDR) read out copy provided by the aircraft operator. See Appendix 2 and 3.

1.12 Wreckage and impact information

Not applicable.

1.13 Medical and pathological

There were no medical aspects relevant to the incident.

1.14 Fire

Not applicable.

1.15 Survival aspects

Not applicable.

1.16 Tests and research

Not applicable.

1.17 Organizational and management information

None

1.18 Additional information

None

1.19 New investigation techniques

None

2. Analyses

Meteorological condition at the passengers boarding time was complicated, changeable weather with shower. Due to rain, the water ingresses into pressurization seal of the entrance door. During aircraft climb temperature quickly fell down. Due to the presence of water in the pressure seal, the water drainage holes possibly were blocked by ice and its cause the failure of the maintaining the pressure in pressure seal of the door. Because of that huge air leakage appears in the area of the entrance door and pressurization system could not maintain normal pressure in the cabin. When the pressure in the cabin reaches the value of the cabin pressure sensor switching the Cabin Alt warning comes on. As well at the pre-set value of cabin pressure oxygen masks automatically dropped out.

The captain decided to perform landing in the Riga International Airport.

During descent outside temperature increases and ice blockage in the door pressurization seal was melted, that restores the normal operation of the pressurization system.

3.  Conclusions

3.1. Findings

1. The aircraft was fully serviceable.

2. The flight crew was properly licensed to perform the flight.

The reason of the decompression in the passenger cabin during the aircraft cruise at FL340 was the entrance door’s pressurization seal drainage holes blockage due to frozen water.

3.1.1. Bay of passenger entrance door where pressurization seal drainage holes blockage due to frozen water.

4. Safety Recommendations 2005-7

In the airline (operator of the aircraft involved in the incident) the procedures to be introduced for strongly monitoring the entrance door opening at the rainy weather conditions. Of course it is understandable that impossible to avoid opening the door at heavy rain. But the door opening to be limited as much as possible and to be monitored by flight crew and/or handling organization.

24.10. 05.

Investigator-in -charge

Head of Division Aircraft Accident and Incident

Investigation Ministry of Transport of the Republic

of Latvia								Ivars Gaveika

Aircraft Accident and Incident Investigator				Ivars Zorgenfreijs

Ministry of the Transport of Latvia

Appendix 1

Radio communication records

Radio communication records

DATE: 19.05.2005

PERIOD: 12.38 - 13.13 (UTC)

ATC UNIT: Riga ACC (East sector, Approach, TWR)

| TIME (UTC) |  | THE RADIOTELEPHONY |
| --- | --- | --- |
| 12.38.36 | Pilot | Riga good afternoon, AUA 612 flight level 340 |
|  | Contr | ADA 612 Riga Control, good afternoon, radar contact |
|  | Pilot | Thank you |
| 12.47.10 | Pilot | A-Austrian 612, Riga |
|  | Contr | Austrian 612 go ahead |
|  | Pilot | Request descend level 150, please |
|  | Contr | AUA 612 say again please, what FL would you like? |
| 12.47.25 | Pilot | Request level 150 |
|  | Contr | AUA 61 2 descend FL 160 |
|  | Pilot | 160, leaving 340 now |
| 12.48.16 | Contr | AUA 61 2 Riga |
|  | Pilot | Go ahead |
|  | Contr | AUA 612 could you tell me please reason for descent? |
|  | Pilot | We have depressurisation problem |
|  | Contr | AUA 612 roger, depressurisation problem, continue descend FL 160 |
|  | Pilot | 160,612 |
| 12.49.57 | Contr | AUA 612 no traffic reported on your heading, continue descend FL 140 |
|  | Pilot | Descend level 140, AUA 612 |
| 12.50.19 | Contr | AUA 612 report your intention |
|  | Pilot | Standby... |
| 12.50.50 | Contr | AUA 61 2 now change frequency please 1 27,3 |
|  | Pilot | 27,3 good bye, AUA 612 |
| 12.50.59 | Pilot | Riga good afternoon, AUA 612 descending FL 140 |
|  | Contr | AUA 612, Riga Approach, good afternoon, radar contact |
|  | Pilot | Thank you |
| 12.51.43 | Contr | AUA 612 Riga Approach confirm you are proceed to destination |
|  | Pilot | Negative sir, we now ... stand by please, we have to decide... |
| 12.52.58 | Contr | AUA 612 would you like descend lower? |
|  | Pilot | Stand by, we are 140 maintaining now |
| 12.53.47 | Pilot | AUA612requestFL100 |
|  | Contr | AUA 61 2 descend level 100 |
|  | Pilot | Descending FL 100, AUA 612 |
| 12.55.30 | Pilot | AUA 61 2 |
|  | Contr | AUA 61 2 |
|  | Pilot | Request immediate to diverting to Riga please |
|  | Contr | AUA 612 expect radar vectoring for ILS 36, you are 33 |

Page 1 of 3

23.05.2005

|  |  | miles from RIX VOR, turn right heading 280, descend to altitude 2500 ft, QNH 1022 |
| --- | --- | --- |
|  | Pilot | 1022, descending 2500 ft and right heading 280 confirm |
|  | Contr | AUA 612 turn right heading 285 now |
|  | Pilot | Right heading 285, RWY 36 Riga |
| 12.56.16 | Pilot | And we declare emergency now - MAYDAY, MAYDAY, MAYDAY, AUA 612, we have problem with cabin altitude, we have depressurisation height now and immediate back to Riga, please |
|  | Contr | AUA 612, roger, MAYDAY, expect priority to land to Riga, RWY in use 36, turn right heading 290 |
|  | Pilot | Right heading 290, AUA 612 |
|  | Contr | AUA 612 confirm do you have aerodrome details? |
|  | Pilot | Say again please |
|  | Contr | AUA 612 copy aerodrome details |
|  | Pilot | Affirm, we have aerodrome details Riga RWY 36 |
|  | Contr | AUA 612 and information Q, wind 320 deg. 8 knots, visibility 10 km, clouds 4900 ft, QNH 1022 |
|  | Pilot | 1022 and we have RWY frequency from Riga aerodrome details, thank you very much |
|  | Contr | AUA 612 continue present heading, descend altitude 2500 feet and request passenger on board, total passenger on board, tankage and dangerous goods |
|  | Pilot | Negative, we have no dangerous goods on board and stand by... we have 57 passengers, I think |
|  | Contr | AUA612confirmP.O.B. 57 |
|  | Pilot | Negative, 5 0 passengers, 5 0 passengers on board and last ... (unreadable) |
|  | Contr | AUA 61 2 roger, 50 |
| 12.59.38 | Contr | AUA 61 2 |
|  | Pilot | Go ahead |
|  | Contr | AUA 612 request the total passenger on board and tankage upon arrival |
|  | Pilot | ...(unreadable) |
|  | Contr | Sorry, say again |
|  | Pilot | ... (unreadable) |
| 13.00.05 | Contr | AUA 612 readability 2 and say again your information |
|  | Pilot | ... (unreadable) |
|  | Contr | AUA 61 2 go ahead |
|  | Pilot | ...(unreadable)... 50 passengers and Stones ...tankage . . . endurance. . . (unreadable) |
|  | Contr | AUA 612, 60 passengers and 5000 fuel confirm |
|  | Pilot | ...(unreadable) |
| 13.00.59 | Contr | AUA 612 continue descend to altitude 2500 feet, you are 18 miles from RIX VOR. AUA 612 minimum safety altitude 2300 feet |
|  | Pilot | AUA 612 we descend to 2500 feet now |
|  | Contr | AUA 612 I read you 5 now and request total passengers on board and tankage upon arrival |
|  | Pilot | We have 5 0 passengers on board and we have 6.1 tones fuel on board |
|  | Contr | AUA 612 roger, 50 passengers on board, 6.1 tones |

Page 2 of 3

23.05.2005.

|  | Pilot | Affirm sir |
| --- | --- | --- |
| 13.01.55 | Contr | ADA 612 do you need special assistance? |
|  | Pilot | Negative, we have only cabin problem, no assistance |
|  | Contr | AUA612 roger |
| 13.02.11 | Contr | AUA 612 turn right heading 295 |
|  | Pilot | Right heading 295.AUA 612 |
| 13.02.48 | Contr | AUA 612 what is total number of crew? |
|  | Pilot | Which total of number? |
|  | Contr | AUA 612 number of crew request |
|  | Pilot | We have crew ...5 crew and 50 passengers on board, AUA 61 2 |
|  | Contr | AUA 61 2 roger, 55 total |
|  | Pilot | Roger |
| 13.03.31 | Contr | AUA 612 you are 11 miles to go, turn right heading 335, cleared ILS approach RWY 36, report localizer established |
|  | Pilot | Right heading 335, cleared ILS approach RWY 36, call you localizer established, AUA 612 |
| 13.04.30 | Contr | AUA 612 do you need any medical assistance? |
|  | Pilot | For the time negative, on ground later-on may be |
|  | Contr | AUA 612 roger, continue approach 9 miles to go, approaching to localizer, report established |
|  | Pilot | Roger cleared for ILS approach RWY 36, we have the field insight, AUA 61 2 |
|  | Contr | AUA 612 are you ready for visual? |
|  | Pilot | Affirm sir |
|  | Contr | AUA 612 continue approach, contact TWR 118.1 |
|  | Pilot | 18.1 bye-bye, 612 |
| 13.05.05 | Pilot | Riga good afternoon, AUA 612 we are visual approach RWY 36,we have field in sight |
|  | Contr | Good afternoon AUA 612,Tower, wind 330 degr. 8 knots cleared to land RWY 36 |
|  | Pilot | Cleared to land AUA 612 |
| 13.08.49 | Contr | AUA 612 are you able to vacate RWY? |
|  | Pilot | Affirm |
|  | Contr | Please say again |
|  | Pilot | Affirm, we leaving the RWY, we need retaxi to the ramp, we need and stairs for disembarkation please |
|  | Contr | AUA 612 vacate to the right E, F, follow "Follow me" car. |
|  | Pilot | E, F behind "Follow me" AUA 612 |
| 13.11.55 | Pilot | AUA 61 2 |
|  | Contr | 612 |
|  | Pilot | We just confirmed we need a stairs for disembarkation and medical assistance, please |
|  | Contr | AUA 612 roger, |
|  | Contr | 612 roger need medical assistance |

LGS SAFETY MANAGER				V.KARETNIKOV

Page 3 of 3

23.05.2005

Appendix 2

Flight Data Recorder (FDR) read out of Serious Incident Austrian Airlines Fokker F28 Mark100, Registration OE-LVI on 19.05.2005 at Riga International Airport (EVRA), Latvia

Appendix 3

Emergency Landing of Fokker F28 Mark100, Registration OE-LVI, on 19.05.2005. at Riga International Airport (EVRA), Latvia

Flight Data Recorder (FDR) read out copy of Serious Incident Flight Number OS 612

Appendix 4

Copy of Maintenance Workorder

Appendix 5

Copy of Technical Aircraft LOG